CLASSIC DASH ADDS

1987-93 MUSTANG

Classic Dash has added the popular 1987-93 “Fox” Mustang to its roster of vehicles that can easily have their functionality and appearance updated with a bolt-in custom dash panel. Dashboards for earlier 1979-86 “Fox” Mustangs are already available from Classic Dash.

The panels are manufactured in-house from UV-resistant ABS composite material and are offered in matte black, brushed aluminum and carbon fiber finishes. They are available plain, or with a full compliment of Auto Meter or Thunder Road gauges (choice of 15 styles) and a wiring kit.

Design wise, the panels come with two 3-3/8" openings for the tach and speedometer, plus four 2-1/16" apertures for auxiliary gauges; most enthusiasts opt for short sweep oil pressure, water temperature, voltage and fuel level—although others are available. They are a bolt-in replacement for the OEM panel, and accommodate factory accessories and trim.

Only commonly available tools are needed for the installation, and it can typically be performed in an afternoon by a competent do-it-yourselfer. A complete dashboard wiring kit that integrates into the OEM harness is available and comes with a detailed 24-page instruction booklet.

For additional information visit the firm’s newly revamped website atwww.ClassicDash.com, or call 775-883-7904. Classic Dash is an industry leader in providing instrumentation solutions for 1960s, 70s, 80s and 90s muscle cars, classic trucks and later model enthusiast vehicles.

-30-